## Slide 1
Mn+1
An
Xn
Where n = 0,1,2,3…
PHASE
DHARAMANANDA SAHA
CUSB2404112015
https://youtu.be/UUhlRWbomyA?si=57b2YRZ9HiyTxHdj
MXene
Under the supervision of
Dr. Rohit Ranjan Shahi

## Slide 2
MXene
MXenes are a class of two-dimensional (2D) nanomaterials composed of transition metal carbides, nitrides, or carbonitrides. These materials are derived from a parent layered compound known as the MAX phase.
The term “MXene” is derived as follows:
M is Early transition metal (Ti, V, Cr, Nb, etc.)
X isCarbon and/or Nitrogen
https://doi.org/10.1016/j.susmat.2022.e00439

## Slide 3
MXene
Type | MAX Phase | M | A | X
211 | Ti2AlC | Ti | Al | C
211 | V2GaC | V | Ga | C
211 | Nb2SnC | Nb | Sn | C
211 | Cr2AlN | Cr | Al | N
312 | Ti3SiC2 | Ti | Si | C
312 | V3AlC2 | V | Al | C
312 | Nb3GeC2 | Nb | Ge | C
312 | Cr3AlN2 | Cr | Al | N
413 | Ti4AlC3 | Ti | Al | C
413 | Nb4SiC3 | Nb | Si | C
413 | V4GaC3 | V | Ga | C
413 | Ti4AlN3 | Ti | Al | N
514 | Mo5AlC4 | Mo | Al | C
514 | Ti5SiC4 | Ti | Si | C
514 | Nb5GaC4 | Nb | Ga | C
514 | V5AlN4 | V | Al | N
Mixing at M-site
Example:
M layer contains:
  50% Ti & 50% Nb
This is called: Solid solution at M-site
Mixing at A-site
Example:
A layer contains : 50% & 50% Si
Mixing at X-site
Example:
X layer contains: 50% Carbon & 50% Nitrogen

## Slide 4
MXene
https://youtu.be/UUhlRWbomyA?si=57b2YRZ9HiyTxHdj
Mn+1​ Transition metal layers (Ti, V, Nb… )
If , then:
Xn​ is Carbon/Nitrogen layers
Tx surface terminations
After synthesis, the surface gets functional groups like:
–O (oxygen) –OH (hydroxyl) –F (fluorine)
–Cl (chlorine)
n=1,2,3…… determines the thickness and structure
Examples:
First MXene:
(Titanium): (Carbon) surface groups (–O, –OH, –F)
Discovered in 2011 at Drexel University
The MAX () phase was immersed in strong etching solution like HF. Converting
surfaces get functional groups: –F (from HF) : –OH (from water): –O (oxidation)

## Slide 5
Synthesis of MXene
https://doi.org/10.1002/adma.201102306
Removal of A-layer:
Formation of –OH Termination
Formation of –F Termination
Etching
Hydroxyl Termination
Fluorine Termination

## Slide 6
MXene
Properties | Advantages | Disadvantages
Electrical & Electronic Properties | MXenes exhibit high electrical conductivity (up to ~10,000 S/cm) due to partially filled d-orbitals of transition metals, enabling efficient electron transport and metallic behavior. | Conductivity degrades upon oxidation as surface Ti (or other metals) forms insulating oxides (e.g., TiO₂), disrupting electron pathways.
Surface Area & Ion Transport | The 2D layered structure provides a high surface-to-volume ratio and hydrophilic surface terminations (–OH, –O), facilitating rapid ion diffusion and high electrochemical capacitance. | Strong van der Waals interactions cause restacking of layers, reducing accessible surface area and hindering ion transport.
Chemical Tunability | Surface terminations (Tₓ = –O, –OH, –F) can be tuned to modify electronic structure, catalytic activity, due to reactive surface sites. | Synthesis typically involves hydrofluoric acid (HF), which is highly toxic and corrosive, posing safety and scalability challenges.

## Slide 7
MXene
Application | how mxene is used ? | Property of mxene | Reference
Supercapacitors | MXenes store charge via pseudocapacitive behavior and electric double-layer formation. Their layered structure allows rapid ion intercalation/de-intercalation. | High conductivity (~10⁴ S/cm) & hydrophilic surface (–OH, –O groups) enables fast ion transport and high capacitance. | Naguib et al., Advanced Materials, 2014 DOI: 10.1002/adma.201304138
Lithium-ion Batteries | MXenes act as anode materials where Li⁺ ions intercalate between layers with minimal diffusion resistance. | Large interlayer spacing & metallic conductivity improves charge transfer and cycling stability. | Lukatskaya et al., Science, 2013 DOI: 10.1126/science.1241488
Electrocatalysis (HER/OER) | Surface terminations and exposed metal sites act as active catalytic centers for hydrogen and oxygen evolution reactions. | Tunable surface chemistry (–O, –OH, –F) & high surface area enhances catalytic activity and lowers overpotential. | Seh et al., Chemical Society Reviews, 2017 DOI: 10.1039/C6CS00631E
Sensors (Gas/Biosensors) | Changes in electrical resistance occur upon adsorption of gas molecules or biomolecules on MXene surface. | High surface reactivity & large surface area provides high sensitivity and fast response time. | Kim et al., ACS Nano, 2018 DOI: 10.1021/acsnano.8b05054
Water Purification | MXenes adsorb heavy metal ions and dyes through electrostatic interaction and surface functional groups. | Hydrophilicity & negatively charged surface enhances adsorption efficiency. | Rasool et al., Nature Communications, 2016 DOI: 10.1038/ncomms12461

## Slide 8
Thank you.